## Slide 1
SMART PARENTING TECHNOLOGY
Baby Monitor
Project
Intelligent monitoring for peace of mind
Team Name | Course / Institution | 2026

## Slide 2
TEAM MEMBERS
Ahd Mohsen
231001691
Sara Saria
231010910
Reem Mahmoud
231001389
Sana Mahmoud
231000371
Layan Mohamed
231002952
Bachelor of Electrical & Computer Engineering
Baby Monitor Project • 2026
2

## Slide 3
PROJECT PHOTOS
Circuit – Top View
Circuit – Side View
Baby Doll (Test Subject)
Circuit – Clean Build
3

## Slide 4
COMPONENTS USED
Arduino Uno
Main microcontroller. Runs the logic, reads sensors, and controls outputs.
MOSFET IRF Z44N
(N-Channel)
Acts as a high-current switch. Gate connected to PWM pin 5 (~5V) to control motor speed. Drain → motor, Source → GND.
Gear Motor (Yellow)
High-torque, low-speed DC motor. Opens/closes the baby bed cover based on sound detection.
Sound Sensor
Analog microphone module. Reads crying/noise via A0. VCC → 5V, GND → GND.
Bluetooth HC-05
Wireless link to parent's phone. VCC → 5V, GND → GND, TXD → Pin 11, RXD → Pin 10.
9V Battery
Powers the gear motor independently. (+) → motor, (−) → common GND.
Baby Doll & Bed
Physical demo setup. The doll simulates a baby; the bed has a motorised cover controlled by the circuit.
Jumper Wires
Connect all components on the breadboard. Colour-coded for clarity.
4

## Slide 5
CIRCUIT WIRING & CONNECTIONS
Arduino (Controller)
5V → Breadboard positive rail
GND → Breadboard negative rail
Sound Sensor (Input)
A0 → Arduino Analog Pin A0 (reads analog cry signal)
VCC → 5V | GND → GND
Bluetooth HC-05
VCC → 5V | GND → GND
TXD → Arduino Pin 11 (receives data)
RXD → Arduino Pin 10 (sends data)
MOSFET IRF Z44N
Gate → PWM Pin 5 (~5V) — controls motor speed
Drain → Gear Motor terminal
Source → GND
Gear Motor
Controlled by MOSFET drain
Opens/closes bed cover on cry detection
High torque ensures reliable actuation
9V Battery
(+) → Gear Motor positive terminal
(−) → Common GND
Separate from Arduino 5V rail for motor current
5

## Slide 6
SYSTEM ARCHITECTURE
Hardware Unit
Arduino Uno (MCU)
Sound Sensor (A0)
MOSFET IRF Z44N
Gear Motor (DC)
9V Battery
Signal Flow
Sound → Analog signal
Arduino processes input
PWM signal to MOSFET
MOSFET switches motor
Bluetooth sends alert
Mobile / Output
HC-05 Bluetooth
Parent's smartphone
Real-time notifications
Motor opens bed cover
Sound threshold control
6

## Slide 7
BLYNK PHOTOS
Circuit – Top View
Circuit – Side View
Blynk uses virtual pins as an IoT interface to communicate between the app and the device. The connection is established using an authentication code, similar to a password, which must be known by both the device and Blynk.
Blynk.write() is used to send data from the app to the Arduino, while Blynk.virtualWrite() sends data from the Arduino to the app. The Blynk.run() function keeps the Blynk connection active and allows continuous communication between the device and the app.
3

## Slide 8
Thank You
Questions & Discussion Welcome
Ahd • Sara • Reem • Sana • Layan